## Slide 1: In-network data collection and processing with TinyOS
Middleware Technologies for Distributed Systems 2020
Saúl Almazán del Pie
Marina Alonso-Cortés Lledó
Jorge Santisteban

## Slide 2: The problem:
Create a sensor network with one central sensor, the sink node, that is informed by the rest of the nodes when the temperature measured by any of them is above a given threshold. The sink node periodically chooses the new threshold and broadcasts a SETUP message, which floods the network (assume a multi-hop scenario).
The SETUP message is used to propagate the new threshold and to setup the routes that must be followed back by DATA messages to reach the sink.
Each sensor periodically measures the temperature and delivers a DATA message toward the sink if the measured value is above the current threshold. DATA messages are sent hop-by-hop toward the sink using point-to-point communication (use the address-based protocol provided by the TinyOS active message layer). The DATA message carries the measured temperature and the identifier of the measuring node.
Assumptions
  Assume DATA messages are rare (i.e., the threshold is high with respect to the average temperature).
Requirements
  Test the system in TOSSIM, with a network big enough to stress the multi-hop nature of the protocol.

## Slide 3: Assumptions we made on the environment’s temperatures
The sensors are supposed to be in a place were temperatures range from 0 to 70 ºC
Thresholds are temperatures in the range 50-70 ºC (so that temperatures above threshold are rare)
We did it like this, but it could easily be changed, and we can show the parts of the code where it would have to be changed:
  In TemperatureMonitorC.nc adjust line:
    threshold = (call Random.rand16() % 20) + 50;
  In TemperatureSensorP.nc adjust line:
    signal Read.readDone(SUCCESS, call Random.rand16()%70);

## Slide 4: Elements
TinyOS network described with:
  TemperatureMonitor
  TemperatureSensor
Topology and noise files:
  topoConfig.txt  creates the “topology.out” and “linkgain.out” files
  Noise files taken from TOSSIM library: “meyer-heavy.txt” and “casino-lab.txt”
2 python scripts for TOSSIM simulations, each using one of the noise files

## Slide 5: TemperatureMonitor
The application running in each node. It has the following elements:
  TemperatureMonitor.h: the header
  TemperatureMonitorAppC.nc: the top level configuration
  TemperatureMonitorC.nc: the main module, includes the actual implementation of all the functionality of the different sensors
  TemperatureSensorC.nc: the top level generic configuration of a secondary module that is used by the main module to read temperatures. It simulates the functionality of a real temperature sensor.
  TemperatureSensorP.nc: the implementation of the module

## Slide 6: TemperatureMonitor.h
Here we included some important macros:
  AM_TEMPERATURE_MONITOR 20  ID for the AM Layer
  MAX_TEMP 70  as explained before we assume max temperature is 70ºC
  TIMER_SINK_PERIOD 30000  period of time between calculations made by sink node to produce new threshold and send new SETUP message
  TIMER_SENSOR_PERIOD 5000  period at which nodes make temperature measurements
    This way nodes are measuring temperatures more often than the threshold is changed.
Message structures for the 2 kind of messages SETUP and DATA

## Slide 7: SETUP message
typedef nx_struct setup_msg_t {
nx_uint16_t msg_id;
nx_uint16_t threshold;
} setup_msg_t;
msg_id : the id of the SETUP message, increments with each new threshold
threshold: the new chosen threshold

## Slide 8: DATA message
typedef nx_struct data_msg_t {
nx_uint16_t node_id;
nx_uint8_t msg_id;
nx_uint16_t temperature;
} data_msg_t;
node_id: the id of the Node that recorded the temperature above threshold
msg_id: id of the message to keep track of temperature measurements
Temperature: the measured temperature

## Slide 9: TemperatureMonitorAppC.nc
Top-level configuration: wires the TemperatureMonitor component to all the other components it uses. These are:
  MainC: used to boot the TemperatureMonitor Module
  3 TimerMilliC for the 3 timers used by the TemperatureMonitor
    TimerSink: when fired, sink node calculates new threshold and sends SETUP
    TimerSensor: when fired, sensor node measures temperature
    WaitingTimer: used to make node wait after receiving SETUP message and before forwarding it
  AMSenderC: provides the Packet, AMPacket and AMSend interfaces to access AM message structure and to send messages through the AM layer
  AMReceiverC: provides the Receive interface to receive messages
  ActiveMessageC: provides the SplitControl (called AMControl in the TemperatureMonitor) to start/stop de AM Layer
  TemperatureSensorC: component to measure temperatures, provides the interface necessary to read temperatures
  RandomC: to generate random numbers for the threshold calculations

## Slide 10: TemperatureSensorC.nc
Top-level configuration of the TemperatureSensor, wires the different components used by it.
It is a generic component because it is not a singleton component. It does not have any arguments in this case.
Uses:
  RandomC: to generate temperature
  TimerMilliC: to simulate the time it would take a real device to measure a temperature
Provides:
  Read interface, so that the TemperatureMonitor uses the TemperatureSensor by reading it: Temperature.read();

## Slide 11: TemperatureSensorP.nc
Implementation of the TemperatureSensor
When the TemperatureSensor is read, it starts one shot on the timer of 10 units of time (the timer will be fired 10 units of time after)
When timer is fired, it reads a random number from 0 to 70

## Slide 12: TemperatureMonitorC.nc
uses {
interface Boot;
interface Packet;
interface AMPacket;
interface AMSend;
interface Receive;
interface SplitControl as AMControl;
interface Read<uint16_t> as Temperature; /* Temperature measurements */
interface Timer<TMilli> as TimerSink; /* Period to send SETUP msg */
interface Timer<TMilli> as TimerSensor; /* Period to meassure Data */
interface Timer<TMilli> as WaitingTimer; /* Makes sensors wait before forwarding SETUP msg*/
interface Random; /* Generates random threshold */
}

## Slide 13: TemperatureMonitorC.nc: variables
Important variables:
  Threshold: to save latest threshold
  Temperature: in child nodes, to save latest read temperature
  maxTemp: in sink node, to keep track of the highest measured temperature for the final statistics made on the simulation
  counter:
    In sink node used to keep track of the number of different SETUP messages that it has sent. Used as ID of the newest sent SETUP message
    On child node: ID of the latest received SETUP message, to ignore the received SETUP messages that are older than the newest received
  dataCounter: on sink node, number of DATA messages received, for final statistics
  sentCounter: total number of messages of any kind sent or forwarded by each node, for final statistics
  measurements: total number of temperature measurements made by child node
  prev_node: on child node, saves the address of the previous node on the route to get back to sink node. When sending or forwarding DATA msgs, each child node will send to the previous node

## Slide 14: TemperatureMonitorC.nc: events
event void Boot.booted(): when a sensor is booted
  Variables are initialized
  Debug message written on “nodes” log
  AMControl started
event void AMControl.startDone(error_t err): when the AM Layer is opened and started
  Debug message written on “nodes” log
  In the sink node, the TimerSink is started with its period
  In child node, the TimerSensor is started with its period
  In case of error, AMControl is started again
event void AMControl.stopDone(error_t err): after stopping the AM Layer
  Debug message written on “nodes” log
  Timers are stopped in each case

## Slide 15: Creating, sending, receiving and forwarding SETUP
TimerSink.fired(): time to calculate new threshold
  New threshold is calculated with the interface provided by RandomC
  sendSETUP() task is posted
task void sendSETUP(): to send a new SETUP msg only the sink node
  Check if it is the sink node, and if it is not busy
  Create new setup message carrying the ID given by the counter variable and the new threshold.
  Send through AMLayer with AMSend on Broadcast address
event message_t * Receive.receive(): when child node receives a SETUP message
  Check it is child node and the message is SETUP msg
  Check it is not an old SETUP message by comparing its ID with the counter
  Save the msg
  Save the address of the sender as the prev_node
  Start on shot of 80+TOS_NODE_ID*15 units of time of the WaitingTimer

## Slide 16: Creating, sending, receiving and forwarding SETUP
WaitingTimer.fired(): time to calculate new threshold
  forwardSETUP() task is posted
task void forwardSETUP(): to forward in broadcast the last received SETUP msg any node
  Check if it is not busy
  Create setup message with the corresponding data
  Send through AMLayer with AMSend on Broadcast address

## Slide 17: Reading temperature, sending new DATA msg and forwarding
SensorTimer.fired(): time to measure new temperature
  Call read on the TemperatureSensor component
event void Temperature.readDone(error_t err, uint16_t val): TemperatureSensor returns a read temperature val
  New temperature with value val saved on node
  Increment number of measurements
  If temperature is above threshold, post task sendData
task void sendDATA(): performed only by child nodes
  Check it is not the sink node and it is not busy
  Create new data message with the counter as msg_id, their own TOS_NOD_ID as node_id, and the temperature
  Send with AMSend to the address of the previous node on the route

## Slide 18: Reading temperature, sending new DATA msg and forwarding
event message_t * Receive.receive(): receiving DATA msg, 2 cases depending if the receiving node is the Sink node or another child
  Sink node: DATA msg has arrived to its destination
    Increment the dataCounter
    Update the maxTemperature
  Child node: must forward data
    If the DATA msg was actually sent to them, they must forward it: post task forwardData()
task void forwardDATA(): performed only by child nodes
  Check it is not the sink node and it is not busy
  Create new data message with the corresponding values
  Send with AMSend to the address of the previous node on the route

## Slide 19: Considerations
There are some scenarios that have been discarded because they were not specifically asked to be considered, but that could happen and could be handled differently.
Consideration 1:
  When sink node receives a DATA msg, it does not know if that data was measured with respect to the last threshold or any other. In our functionality it did not really matter because we are not really doing anything with the temperatures received by the sink node, except keeping track of the maximum recorded temperature.
  If we had wanted to have this information, we could have added another field in the data_msg_t to hold the threshold associated with that temperature
Consideration 2:
  The virtual time of the Virtual Machine is not the same as the computers time.
  Using the functions ticksPerSecond() and time() and the conversion formulas shown in class by the teachers, we are not able to print the info each 10 seconds. The information prints much faster and time passes much faster.
  We could have adjusted the conversions in the simulation to make it run slower but then the code would formally be wrong, so we decided to keep the code right even if the result doesn’t run at the rhythm it should.

## Slide 20: Debugging
There are three debugging channels:
  Nodes: where we write information regarding actions that happen on the nodes, like starting/stopping the components, new temperatures read, new threshold calculated, or actions that the nodes have to do, like forwarding
  Radio: we write information regarding the AM Layer, that is: sent, forwarded or received events.
  Errors: for possible errors
These channels can be printed in the simulation or not depending on the information one is interested in

## Slide 21: Simulations
2 simulations: run1.py and run2.py
14 nodes
120 seconds of simulation (seems a lot but because the simulation on the virtual machine run faster than expected it was the only way of actually making the simulation long enough to see results)
Topology file is "linkgain.out”
Noise files:
  In Simulation 1 it is “meyer-heavy.txt”
  In Simulation 2 it is “casino-lab.txt”

## Slide 22: Steps in the simulation
Create a connection to the Nesc app TimerMonitorAppC and a new tossim radio
Add gain links and noise trace
Boot the nodes sequentially each 10 ms after the previous.
Connect TimerMonitorC variables to python variables to be able to obtain information collected by the nodes
Each 10 seconds of simulation we print:
  The number of SETUP messages sent and DATA msgs received by the Sink in the 10 seconds of simulation
  Total number of msgs exchanged in the system in those 10 seconds
When simulation time ends we compute
  Total exchanged messages
  Maximum number of exchanged msgs in a 10 s time period
  Minimum number of exchanged msgs in a 10 s time period
  Average number of exchanged msgs in a 10 s time period
  Total number of SETUP msgs sent by Sink
  Total number of DATA msgs received by Sink
  Total number of temperature measurements
  Highest recorded temperature
  Percentage of temperatures above threshold